3-WHEEL 2010 ELECTRIC TRIDENT VAN WITH AIR/CON

IDEAL FOR TAXI OK FOR USA BUILT TO DOT SPEC

SPECIFICATIONS

| Key Specifications | Chassis |
| --- | --- |
| Model | EPV-85120 | Suspension | Front Duel Coil Spring, Rear Plates Spring |
| Drive Train | Rear Wheel Drive | Steering System | Power Assisted Steering |
| L/W/H (mm) | 3400/1440/1600 | Tire Size | 155/R13 |
| Wheelbase (mm) | 2080 | Aluminum Alloy Rim | 13”(Rear) |
| Grand clearance (Full Loaded) | 160 mm | Safety |
| Top Speed (KPH) and Range | >90KM/H Max Range 100KM | All-Steel Welded Body Construction |
| Electricity Consumption | 15KWH | Seat Belts |
| Transmission | Automatic | High Mounted Brake lamps |
| Electric Motor | Front and Rear Fog Lights |
| Motor | 8.5KW AC Motor | Front Disc/Rear Drum Brake |
| Controller | 400Amp | Configuration |
|  |  | Power Door Locks |
| Power and Battery | Power Windows |
| Rated Power | 8.5KW | Sliding Side Door |
| Max. Torque | 100N.m | Triple Stitched Comfort Vinyl Seats |
| Max Motor Speed | 5000RPM | Spare Tire |
| Batteries | 10x12pieces 150Ah Maintenance Free | Radio(FM/AM) +MP3 (USB)/CD/VCD/DVD Player |
| Weight and Load Capacity | Heater and Air Conditioner-Cooler |
| Gross Vehicle Weight | 1100 KGS | Roof Window |
| Seats | 4 seats with rear removable bench | Color Choice |
|  |  | Body: Red, White, Black, Yellow, Blue, Silver Interior: Tan or Gray |

Price: with air conditioning US$7,800.00/vehicle (4 vehicles in 45feet container)

Freight Cost Not Included

Photo Gallery